## Slide 1: AMIT Embedded Systems Diploma Graduation Project.
Electric Water Heater

## Slide 2: Team Members
Hatim Mahmoud Mohammed AbdElHady Ghonaim.
Tareq Usama Saad Mohammed AbdElRahman.
Ahmed Saleh Mohammed Mahmoud.
Deema Mohanned Abd El Wahab.

## Slide 3: Table of Contents
Hardware
Software
Software Layered Architecture
LIB
MCAL Drivers
HAL Drivers
APP

## Slide 4
HARDWARE

## Slide 5: Hardware (Simulated Using Proteus)
This project employs AVR ATmega32 microcontroller.
Temperature sensor.
Heating & Cooling Elements.
LEDs
Buttons
7-Segment Display

## Slide 6
SOFTWARE

## Slide 7: Software Layered Architecture.
HAL
APP
MCAL
LIB

## Slide 8: LIB Layer
In this application we used the following Libraries:
STD_Type which provides standard types for precise control over variable sizes, allowing for consistent management of variables
BITMath which contains the macro like functions responsible for manipulating the bits.
Vect_table which defines interrupt service routine (ISR) macros and assigns corresponding vector numbers to specific interrupt events.

## Slide 9: MCAL Drivers
In this application we use the following MCAL Drivers:
ADC (Analog to Digital Converter).
DIO (Digital Input Output).
Internal_EEPROM
GIE (Global Interrupt Enable).
EXIT (External Interrupt).
TIMER0
TIMER1

## Slide 10: MCAL Drivers (cont.)
The ADC Driver is used to convert analog signals from temperature sensor to digital signal to be dealt with using microcontroller.
The DIO Driver is used to control the direction (INPUT or OUTPUT) and value (HIGH or LOW) of microcontroller pins.
The Internal_EEPROM driver is used to store and retrieve the set temperature value used in our system.
The GIE is used to enable the Global Interrupt.
The EXIT Driver is used to control external interrupts connected to the switches.

## Slide 11: MCAL Drivers (cont.)
TIMER0 Driver is used to get the reading from the temperature sensor every 100ms.
TIMER1 driver is responsible for counting a 5-second interval to determine the system's setting mode, controlling the status of the heating element LED with a one-second blink when the heating element is active, and blinks the seven-segment display during temperature setting every one second.

## Slide 12: HAL Drivers
In this application we used the following HAL Drivers:
SSD (7-Segment Display).
Heater_Cooler.

## Slide 13: SSD (7-Segment Display)
In this driver there are 2 files:
SEVEN_SEGMENT_interface.h
SEVEN_SEGMENT_interface.c

## Slide 14: SEVEN_SEGMENT_interface.h
The SEVEN_SEGMENT_interface.h file includes function prototypes for initializing, enabling, disabling, toggling, and writing to the 7-Segment Display.
#ifndef SEVEN_SEGMENT_INTERFACE_H_
#define SEVEN_SEGMENT_INTERFACE_H_
void SSD_Vid_Init();
void SEVEN_SEGMENT_Write_Val(u8 number);
void SSD_DIS();
void SSD_EN();
void SSD_TOGGLE();
#endif /* SEVEN_SEGMENT_INTERFACE_H_ */

## Slide 15: SEVEN_SEGMENT_interface.c
The SEVEN_SEGMENT_interface.c file includes library dependencies and contains the implementations of functions for the 7-Segment Display.
#include "../../LIB/BITMATH.h"
#include "../../LIB/STD_Type.h"
#include "../../MCAL/DIO/DIO_private.h"
#include "../../MCAL/DIO/DIO_interface.h"

## Slide 16: void SSD_Vid_Init()
This SSD_Vid_Init() function is used to Set the direction of 7-Segment Display Pins as OUTPUT.
void SSD_Vid_Init()
{
DIO_Vid_Set_Port_Dir(PORTC, PORT_OUTPUT);
DIO_Vid_Set_Pin_Dir(PORTA, PIN1, OUTPUT);
DIO_Vid_Set_Pin_Dir(PORTA, PIN2, OUTPUT);
DIO_Vid_Set_Pin_Dir(PORTA, PIN3, OUTPUT);
DIO_Vid_Set_Pin_Dir(PORTB, PIN0, OUTPUT);
DIO_Vid_Set_Pin_Dir(PORTB, PIN5, OUTPUT);
DIO_Vid_Set_Pin_Dir(PORTB, PIN6, OUTPUT);
DIO_Vid_Set_Pin_Dir(PORTB, PIN7, OUTPUT);
DIO_Vid_Set_Pin_Dir(PORTC, PIN7, OUTPUT);
}

## Slide 17: void SSD_EN(), void SSD_DIS(), void SSD_TOGGLE()
These SSD_EN(), SSD_DIS(), SSD_TOGGLE() functions take no arguments and have no return.
The SSD_EN() function is used to set the value of the enable pin of 7-Segment Display to HIGH.
The SSD_DIS() function is used to set the value of the enable pin of 7-Segment Display to LOW.
The SSD_Toggle() function is used to toggle the state of the enable pin of 7-Segment Display between HIGH & LOW.
void SSD_EN()
{
DIO_Vid_Set_Pin_Val(PORTC, PIN7, LOW);
}
void SSD_DIS()
{
DIO_Vid_Set_Pin_Val(PORTC, PIN7, HIGH);
}
void SSD_TOGGLE()
{
DIO_Vid_Toggle_Pin_Val(PORTC, PIN7);
}

## Slide 18: void SEVEN_SEGMENT_Write_Val(u8 number)
This SEVEN_SEGMENT_Write_Val(u8 number) function takes a number as an argument and have no return.
The SEVEN_SEGMENT_Write_Val(u8 number) function is used to convert a two-digit number to its units and tens components and display them on dual 7-Segment Display.
void SEVEN_SEGMENT_Write_Val(u8 number)
{
u8 num[10] = {0x3F, 0x6, 0x5B, 0x4F, 0x66, 0x6D, 0x7D, 0x7, 0xFF, 0x67};
u8 SSD1 = num[number % 10];
u8 SSD2 = num[number / 10];
DIO_Vid_Set_Pin_Val(PORTC, PIN0, GET_BIT(SSD1, 0));
DIO_Vid_Set_Pin_Val(PORTC, PIN1, GET_BIT(SSD1, 1));
DIO_Vid_Set_Pin_Val(PORTC, PIN2, GET_BIT(SSD1, 2));
DIO_Vid_Set_Pin_Val(PORTC, PIN3, GET_BIT(SSD1, 3));
DIO_Vid_Set_Pin_Val(PORTC, PIN4, GET_BIT(SSD1, 4));
DIO_Vid_Set_Pin_Val(PORTC, PIN5, GET_BIT(SSD1, 5));
DIO_Vid_Set_Pin_Val(PORTC, PIN6, GET_BIT(SSD1, 6));
DIO_Vid_Set_Pin_Val(PORTA, PIN1, GET_BIT(SSD2, 0));
DIO_Vid_Set_Pin_Val(PORTA, PIN2, GET_BIT(SSD2, 1));
DIO_Vid_Set_Pin_Val(PORTA, PIN3, GET_BIT(SSD2, 2));
DIO_Vid_Set_Pin_Val(PORTB, PIN0, GET_BIT(SSD2, 3));
DIO_Vid_Set_Pin_Val(PORTB, PIN5, GET_BIT(SSD2, 4));
DIO_Vid_Set_Pin_Val(PORTB, PIN6, GET_BIT(SSD2, 5));
DIO_Vid_Set_Pin_Val(PORTB, PIN7, GET_BIT(SSD2, 6));
}

## Slide 19: Heater_Cooler
In this driver there are 3 files:
Heater_Cooler_Config.h
Heater_Cooler.h
Heater_Cooler.c

## Slide 20: Heater_Cooler_Config.h
This Heater_Cooler_Config.h file contains definitions of Heating/Cooling Elements ports and pins.
#ifndef HEATER_COOLER_CONFIG_H_
#define HEATER_COOLER_CONFIG_H_
#define HEATINGELEMENTLED_PORT PORTD
#define HEATINGELEMENTLED_PIN PIN0
#define HEATINGELEMENT_PORT PORTD
#define HEATINGELEMENT_PIN PIN1
#define COOLINGELEMENT_PORT PORTD
#define COOLINGELEMENT_PIN PIN4
#endif /* HEATER_COOLER_CONFIG_H_ */

## Slide 21: Heater_Cooler.h
This Heater_Cooler.h file contains prototypes of functions to:
Initialize Heating/Cooling Unit.
Turn On/Off Heating element.
Turn On/Off and toggle Heating element LED.
Turn On/Off Cooling element.
#ifndef HEATER_COOLER_H_
#define HEATER_COOLER_H_
void Heater_Cooler_Init();
void Heating_ElementLed_ON();
void Heating_ElementLed_OFF();
void HeatingElement_Led_TOGGLE();
void HeatingElement_ON();
void HeatingElement_OFF();
void CoolingElement_ON();
void CoolingElement_OFF();
#endif /* HEATER_COOLER_H_ */

## Slide 22: Heater_Cooler.c
This Heater_Cooler.c file contains libraries includes and functions implementations.
#include "../../LIB/BITMATH.h"
#include "../../LIB/STD_Type.h"
#include "../../MCAL/DIO/DIO_private.h"
#include "../../MCAL/DIO/DIO_interface.h"
#include "Heater_Cooler_Config.h"
#include "Heater_Cooler.h"

## Slide 23: void Heater_Cooler_Init()
void Heater_Cooler_Init()
{
DIO_Vid_Set_Pin_Dir(HEATINGELEMENTLED_PORT, HEATINGELEMENTLED_PIN, OUTPUT);
DIO_Vid_Set_Pin_Dir(HEATINGELEMENT_PORT, HEATINGELEMENT_PIN, OUTPUT);
DIO_Vid_Set_Pin_Dir(COOLINGELEMENT_PORT, COOLINGELEMENT_PIN, OUTPUT);
}
This Heater_Cooler_Init() function takes no arguments and has no return
This Heater_Cooler_Init() function is used to Set the direction of Cooling element, Heating element and Heating element LED as OUTPUT.

## Slide 24: void Heating_ElementLed_ON(), void Heating_ElementLed_OFF(), void HeatingElement_Led_TOGGLE()
void Heating_ElementLed_ON()
{
DIO_Vid_Set_Pin_Val(HEATINGELEMENTLED_PORT, HEATINGELEMENTLED_PIN, HIGH);
}
void Heating_ElementLed_OFF()
{
DIO_Vid_Set_Pin_Val(HEATINGELEMENTLED_PORT, HEATINGELEMENTLED_PIN, LOW);
}
void HeatingElement_Led_TOGGLE()
{
DIO_Vid_Toggle_Pin_Val(HEATINGELEMENTLED_PORT, HEATINGELEMENTLED_PIN);
}
These Heating_ElementLed_ON(), Heating_ElementLed_OFF(), HeatingElement_Led_TOGGLE(), functions take no arguments and have no return. The Heating_ElementLed_ON()function is used to turn on the LED by setting the HEATINGELEMENTLED_PIN to HIGH. The Heating_ElementLed_OFF()function is used to turn off the LED by setting the HEATINGELEMENTLED_PIN to low. The HeatingElement_Led_TOGGLE() function is used to toggle the value of the HEATINGELEMENTLED_PIN.

## Slide 25: void HeatingElement_ON(), void HeatingElement_OFF()
The HeatingElement_ON() and HeatingElement_OFF() functions take no arguments and have no return. The HeatingElement_ON() function is used to turn on the heating element. The HeatingElement_OFF() function is used to turn off the heating element.
void HeatingElement_ON()
{
DIO_Vid_Set_Pin_Val(HEATINGELEMENT_PORT, HEATINGELEMENT_PIN, HIGH);
}
void HeatingElement_OFF()
{
DIO_Vid_Set_Pin_Val(HEATINGELEMENT_PORT, HEATINGELEMENT_PIN, LOW);
}

## Slide 26: void CoolingElement_ON(), void CoolingElement_OFF()
The CoolingElement_ON() and CoolingElement_OFF() functions take no arguments and have no return. The CoolingElement_ON() function is used to turn on the cooling element. The CoolingElement_OFF() function is used to turn off the cooling element.
void CoolingElement_ON()
{
DIO_Vid_Set_Pin_Val(COOLINGELEMENT_PORT, COOLINGELEMENT_PIN, HIGH);
}
void CoolingElement_OFF()
{
DIO_Vid_Set_Pin_Val(COOLINGELEMENT_PORT, COOLINGELEMENT_PIN, LOW);
}

## Slide 27: Application
This application consists of 3 files:
System_config.h
System.h
System.c

## Slide 28: System_config.h
In System_config.h file we define ports and pins and define magic numbers used in our code.
Additionally, we establish the initial values of variables that may be modified later.
The variable OF_Count is declared as an external variable, and it is utilized from the Timer driver to monitor its value.
#ifndef SYSTEM_CONFIG_H_
#define SYSTEM_CONFIG_H_
#define ON_OFF_PORT PORTD
#define ON_OFF_PIN PIN2
#define UP_BUTTON_PORT PORTD
#define UP_BUTTON_PIN PIN3
#define DOWN_BUTTON_PORT PORTB
#define DOWN_BUTTON_PIN PIN2
#define TEMP_SENSOR_PIN PIN0
#define LED_ON 0
#define LED_BLINK 1 #define SYSTEM_OFF 0
#define SYSTEM_ON 1 #define TEMP_INIT 60
#define TEMP_MARGIN 5
extern u32 OF_Count ;
u8 System_Mode= SYSTEM_OFF;
u8 Temp_Set = TEMP_INIT;
u16 Temp_Curr = TEMP_INIT;
u8 Temp_AVG = TEMP_INIT; #endif /* SYSTEM_CONFIG_H_ */

## Slide 29: System.h
In System.h file we put the prototypes of our functions.
#ifndef SYSTEM_H_
#define SYSTEM_H_
void System_Init();
void Temperature_Setting();
void ON_OFF_Behaviour();
void Temperature_Sensing();
void Heater_Cooler_Control();
void Seven_Segments();
void Temperature_Setting_Up();
void Temperature_Setting_Down();
void TemperatureMonitoringTask();
void EEPROM_Init();
void ADC_Reading_Timer();
#endif /* SYSTEM_H_ */

## Slide 30: System.c
In System.c file we:
Include libraries, drivers, and other header files.
Declare and initialize global variables.
Put the definitions of functions.
#include "../LIB/BITMATH.h"
#include "../LIB/STD_Type.h"
#include "../MCAL/DIO/DIO_interface.h"
#include "../MCAL/ADC/ADC_interface.h"
#include "../MCAL/Interrupts/GIE_interface.h"
#include "../MCAL/Interrupts/EXIT_interface.h"
#include "../MCAL/Internal_EEPROM/EEPROM.h"
#include "../MCAL/TIMER0/TIMER0_interface.h"
#include "../MCAL/TIMER1/TIMER1_interface.h"
#include "../HAL/SevenSegment/SEVEN_SEGMENT_interface.h"
#include "../HAL/Heating_Cooling_Elements/Heater_Cooler_Config.h"
#include "../HAL/Heating_Cooling_Elements/Heater_Cooler.h"
#include "System_Config.h"
#include "System.h"
#define F_CPU 16000000UL
#include "util/delay.h“
/* Global Variables to be used in our system */
u8 SettingMode_Flag = 0;
u8 counter_5sec = 0;
u8 counter_up = 0;
u8 counter_down = 0;

## Slide 31: void System_Init()
The System_Init() function takes no arguments and has no return.
In System_Init() function we:
Enable Global Interrupt.
Initialize External interrupts.
Set Directions of On/Off, Up and Down switches pins.
void System_Init()
{
/*Global Interrupt */
GIE_Vid_Enable();
/* External Interrupt 0 */
EXT_Vid_Interrupt_Init0(RISING_EDGE);
EXT_Vid_Interrupt0();
EXT_Vid_Set_CallBack(Temperature_Setting_Up);
/*External Interrupt 1*/
EXT_Vid_Interrupt_Init1(RISING_EDGE);
EXT_Vid_Interrupt1();
EXT_Vid_Set_CallBack_2(Temperature_Setting_Down);
/*External Interrupt 2 for Switching ON/OFF System */
EXT_Vid_Interrupt_Init2(RISING_EDGE);
EXT_Vid_Interrupt2();
EXT_Vid_Set_CallBack_3(ON_OFF_Behaviour);
/* Switch ON/OFF Direction */
DIO_Vid_Set_Pin_Dir(UP_BUTTON_PORT, UP_BUTTON_PIN, INPUT);
DIO_Vid_Set_Pin_Dir(DOWN_BUTTON_PORT, DOWN_BUTTON_PIN, INPUT);
DIO_Vid_Set_Pin_Dir(ON_OFF_PORT, ON_OFF_PIN, INPUT);

## Slide 32: void System_Init() (cont.)
Initialize Heater/Cooler Unit and 7-Segment Display.
Initialize Analog to Digital Converter and its interrupt.
Initialize Timer 0 in Normal Mode.
Initialize Timer 1 in Normal Clear Timer on Compare Mode.
In addition to our callback functions being triggered with every interrupt
Heater_Cooler_Init();
/*Seven Segment Initialization */
SSD_Vid_Init();
/* ADC Initialization */
ADC_Vid_Init();
/* ADC Interrupt */
ADC_Vid_Interrupt_Enable();
ADC_Set_Call_Back(Temperature_Sensing);
/* Timer0 Normal */
TIMER0_Vid_Interrupt_Enable_Every(100); // 100 ms
TIMER0_Vid_Set_CallBack(ADC_Reading_Timer);
/*Timer 1 CTC*/
TIMER1_Vid_CTC_Init();
TIMER1_Vid_CTC_InterruptEnable();
Timer1_CTC_SetCallBack(TemperatureMonitoringTask);
}

## Slide 33: void ADC_Reading_Timer()
The ADC_Reading_Timer() function takes no arguments and has no return.
In ADC_Reading_Timer() function we:
we initialize a counter variable and increment it with each function call.
Which triggers an ADC measurement every 100 ms.
void ADC_Reading_Timer()
{
static u16 counter1 = 0;
counter1++;
if (counter1 == OF_Count) // 100 ms
{
counter1 = 0;
ADC_Vid_Start_Conversion(ADC0);
}
}

## Slide 34: void Temperature_Setting_Up()
The Temperature_Setting_Up() function takes no arguments and has no return.
In Temperature_Setting_Up() function :
Upon button press, the system checks its status. If the system is on, it enters the setting mode and increments the temperature by 5.
The new set value is then stored in the Internal_EEPROM.
If the system is off, no action is taken.
void Temperature_Setting_Up()
{
if (counter_up != 0)
{
if (System_Mode == SYSTEM_ON)
{
counter_5sec = 0;
Temp_Set += 5;
if (Temp_Set >= 75)
{
Temp_Set = 75;
}
EEPROM_Send(0, Temp_Set);
}
}
else
{
counter_up++;
counter_5sec = 0;
}
}

## Slide 35: void Temperature_Setting_Down()
The Temperature_Setting_Down() function takes no arguments and has no return.
In Temperature_Setting_Down() function :
Upon button press, the system checks its status. If the system is on, it enters the setting mode and decrements the temperature by 5.
The new set value is then stored in the Internal_EEPROM.
If the system is off, no action is taken.
void Temperature_Setting_Down()
{
if (counter_down != 0)
{
if (System_Mode == SYSTEM_ON)
{
counter_5sec = 0;
Temp_Set -= 5;
if (Temp_Set <= 35)
{
Temp_Set = 35;
}
EEPROM_Send(0, Temp_Set);
}
}
else
{
counter_down++;
counter_5sec = 0;
}
}

## Slide 36: void ON_OFF_Behaviour()
The ON_OFF_Behaviour() function takes no arguments and has no return.
The ON_OFF_Behaviour() function :
Toggles the system state from on to off and vice versa.
To turn off the system, the 7-Segment display is disabled, the heating and cooling elements are switched off, the heating element LED is turned off, and the System_Mode variable is set to the SYSTEM_OFF state.
void ON_OFF_Behaviour()
{
if (System_Mode == SYSTEM_OFF)
{
Temp_Set = EEPROM_Recieve(0);
System_Mode = SYSTEM_ON;
}
else
{
SSD_DIS();
Heating_ElementLed_OFF();
CoolingElement_OFF();
HeatingElement_OFF();
EEPROM_Send(0, Temp_Set);
System_Mode = SYSTEM_OFF;
}
}

## Slide 37: void Temperature_Sensing()
The Temperature_Sensing() function takes no arguments and has no return.
The Temperature_Sensing() function :
Converts the sensor reading to decimal appropriate format using the Analog-to-Digital Converter output in an equation.
Then it calculates the current temperature by averaging over 10 values.
void Temperature_Sensing()
{
static u8 counter2 = 0;
static u16 Temp_Sum = 0;
if (System_Mode == SYSTEM_ON)
{
counter2++;
Temp_Curr = ADC_u16_Read() * (float)500 / 1024;
Temp_Sum += Temp_Curr;
if (counter2 == 10)
{
counter2 = 0;
Temp_AVG = Temp_Sum / 10;
Temp_Sum = 0;
Heater_Cooler_Control();
}
}
}

## Slide 38: void Heater_Cooler_Control()
The Heater_Cooler_Control() function takes no arguments and has no return.
The Heater_Cooler_Control() function :
Controls the heating and cooling system based on the required temperature (Temp_Set) and the average room temperature (Temp_AVG).
If the current water temperature (Temp_AVG) is lower than the set temperature by 5 degrees (TEMP_MARGIN), the heating element will be activated, and the cooling element will be deactivated.
If the current water temperature (Temp_AVG) is higher than the set temperature by 5 degrees (TEMP_MARGIN), the heating element will be deactivated, and the cooling element will be activated.
If the both temperatures are equal, turn off both cooling and heating elements.
void Heater_Cooler_Control()
{
if( ( Temp_Set<Temp_AVG+TEMP_MARGIN ) && (Temp_Set>Temp_AVG-TEMP_MARGIN) )
{
HeatingElement_OFF();
CoolingElement_OFF();
}
else if(Temp_Set >Temp_AVG - TEMP_MARGIN )
{
HeatingElement_ON();
CoolingElement_OFF();
}
else if (Temp_Set < Temp_AVG + TEMP_MARGIN)
{
HeatingElement_OFF();
CoolingElement_ON();
}
}

## Slide 39: void TemperatureMonitoringTask()
The TemperatureMonitoringTask() function takes no arguments and has no return.
The TemperatureMonitoringTask() function :
It is triggered every second, specifically designed to facilitate the blinking of the 7-segment display when in set mode
Ensures the LED blinks every second, providing visual feedback when the heating element is active.
void TemperatureMonitoringTask()
{
if ((System_Mode == SYSTEM_ON) && (DIO_u8_Get_Pin_Val(HeatingElement_PORT, HeatingElement_PIN) == HIGH))
{
HeatingElement_Led_TOGGLE();
}
else
{
Heating_ElementLed_OFF();
}
if (SettingMode_Flag == 1)
{
SSD_TOGGLE();
}

## Slide 40: void TemperatureMonitoringTask()(cont.)
In Set mode it displays the current temperature on the 7-Segment Display.
It actively monitors the behavior of the Setting mode, providing updates every 5 seconds whether the user exits the setting mode or not.
if (System_Mode == SYSTEM_ON)
{
counter_5sec++;
_delay_ms(50);
if (counter_5sec > 5)
{
counter_up = 0;
counter_down = 0;
SSD_EN();
SEVEN_SEGMENT_Write_Val(Temp_AVG);
SettingMode_Flag = 0;
}
else
{
SSD_EN();
SEVEN_SEGMENT_Write_Val(Temp_Set);
SettingMode_Flag = 1;
}
}
}